Dune NvmeStorage
Dune NVMe Storage System

Project	DuneNvme
Date	2020-05-21
Reference	DuneNvme/Readme
Author	Dr Terry Barnaby

# Introduction
This directory contains the source code for the Dune NvmeStorage system together with a simple NVMe test environment that allows experimentation with the low level PCIe NVMe interfaces as available on a Xilinx FPGA environment.
The directory contains the FPGA VHDL source code, simulation environment and build environment for the Nvme test FPGA firmware as well as the nvme_test host software.
# Directories
src	The main VHDL source code
src/ip	IP cores generated with Vivado
sim	The simulation environment
vivado	The build environment
test	Host test programs accessing the FPGA firmware
docsrc	Source for the documentation
doc	Output for the documentation

# Test Program
The test Linux host program is in the test directory and is called nvme_test. This program communicates with an NVMe device through the FPGA connected to the host machines PCIe bus. This program allows experimentation with the NVMe low level PCIe interface.
It uses a simple Linux driver, bfpga, whose source code is included in the test directory.
# Building the FPGA bit file and programming
1. cd vivado
2. make clean
3. make all
4. make program
# To Simulate FPGA
1. cd sim
2. Edit Makefile and testbench files for simulation required
3. make
4. make view
# Building the source code
1. cd test
2. make clean
3. make driver
4. make
# More Information
See the DuneNvmeStorageManual and DuneNvmeStorageDesign documents for more information.