Dune NVMe Storage Manual
Preliminary

Project	DuneNvme
Date	2020-05-13
Reference	DuneNvmeStorageManual
Version	0.6
Author	Dr Terry Barnaby

# Introduction
This document covers the use of the Dune NVMe Storage Fpga core and testing thereof. There is also a design level manual, DuneNvmeStorageDesign which covers detailed implementation information and general notes.
# NvmeStorage core overview
The Dune NvmeStorage FPGA core provides the ability to store a data stream of 4 kByte blocks to two Nvme storage devices working in parallel at a rate of 4 GBytes/sec or greater. While performing this it allows the stored data to be read out at a slower rate.
The NvmeStorage core is designed to be controlled by a set of registers from a CPU. An Axi4-lite bus interface provides this ability. It’s data input is designed to come from a raw FPGA binary bit stream using an AXI4 stream interface.
As well as providing data storage, the module also provides direct access to the Nvme devices from a host computer so that statistics and other housekeeping information can be obtained and the Nvme’s controlled. This interface is also useful for test purposes. Two AXI4 streams, one sending a form of PCIe TLP packets to the module from the host and one sending packets to the host from the module provide this ability. It is expected that these AXI4 streams would be sent to a host’s CPU over DMA stream interfaces, possibly multiplexed with packets from other FPGA systems.
# Dune System Overview
The Dune Neutrino experiment has two neutrino detection chambers. Each chamber has a matrix of wires and electronics to amplify and digitise signals captured from neutrino interactions in the chambers. The digitised data is passed through optical fibres to 300 FPGA data processing engines installed in conventional x86 computer servers. The fibres to each FPGA carry around 60 GBits/s of data plus extra bits for encoding overheads.
The Dune project will be designing a custom FPGA board to be installed into the multiple host server computers. This FPGA board will convert the optical data streams to electrical signals, compress and process this data. Currently a simple compression algorithm is proposed that provides around a 2:1 compression ratio. The resulting 3.5 GBytes/s, approx, data stream will be stored in a DDR4 RAM based buffer that can store up to 10 seconds worth of data.
The overall requirement of the NvmeStorage core is to store, real-time, the raw data stream from the Dune system and be able to, with a slower access rate, read that data. The full system is able to store 120 TeraBytes of incoming data at a rate of 600 GigaBytes per second across its multiple FPGA based data processing engines.
For each FPGA engine the source data consists of fixed sized chunks (bursts) of data that are from 20 to 200 GBytes in size. These data chunks are stored, round robin fashion, into the NVMe devices with a new chunk overwriting the oldest chunk written.
The host server computer controls the overall operation of the system via a PCIe interface. It is able to lock a particular chunk in NVMe storage against subsequent writes if it contains data of interest. The data from this chunk can then be read out by the host computer.
## Dune Raw Data
For information, the raw data from the Dune sensors consist of 2560 wires sampled with 12 bits resolution. A super packet containing 64 sets of this data will likely be generated, that includes a start time field and other control information. This will yield data packets of a size near 128 kBytes after compression.
The NvmeStorage core will store data with a block size granularity of 4 kBytes. If an NVMe error occurs, maybe due to a large block write latency or other error, the system will continue storing data, if it can, keeping the block numbers consistent. This means that there could be a set of blocks with in-valid data. So some method of determining if a packet of data is corrupt is needed. The compression algorithm used will provide variable length blocks. We suggest using a variable length packet with CRC checksum padded to a 4 kByte boundary. So a data packet for 64 * 2560 x 12 bit wire samples could look line:
Item	Length	Notes
Length	32 bits	The compressed data length in bytes (packet length is this field + timestamp + misc header length + CRC length).
Timestamp	64 bits	Timestamp for data
Misc	?	Extra header information as needed
Compressed samples	~122 kBytes	The compressed data for 64 samples of 2560 wires at 12 bit resolution.
CRC	32 bits	CRC32 checksum
Padding	?	Padding to next 4/8 kByte boundary

The actual packet format is irrelevant to the NVMe storage system. It simply stores data in blocks to a 4 kByte boundary. However, due to possible latency issues the NVMe may have to drop data and this needs to be handled in a way that allows the host software to use the resulting data stream and understand when data has been lost. To do this the data stream needs to be blocked into some sized packet with a suitable header and dropped at that chunk size.
Two possible methods are:
1. Store and drop at the super packet (128 kByte) level.
2. Store and drop at the storage packet 4 kBytes level, the same as the underlying NvmeStorage block size. Ideally this 4 kByte block would have some header to allow the software to understand if some of these 4 k packets are missing. This could be two 16bit values: the super packet number and the 4k packet number within the super packet.
When a 4k block is sent across the AXI4-Stream, the tlast signal will need to be set in the last clock cycle of the block.
# NvmeStorage core operation
On the reset hardware line driven high or the reset bit in the control register set high the NvmeStorage system will enter an initialisation state. During this state either the core or, if wanted, the host computer will configure the NVMe devices for operation. Once initialised the core is ready to accept commands from the software running on the host computer and the host can perform Nvme reads and writes.
A new data chunk is started by setting the DataChunkStart and DataChunkSize registers to the starting block number and the number of blocks to store. Once set the dataEnable register bit in the Control register is set high to begin writing the data stream to the Nvme devices. Data will be written to the NVMe devices until either the dataEnable register bit is reset or the number of data blocks written equals the programmed DataChunkSize.
The NvmeCore will respond to data read requests as commanded by the host CPU writing to the read control registers or directly to the Nvme device.
## NVMe Storage Access
The NvmeStorage uses a block size of 4 kBytes. The NVMe storage use a simple integer block number to address the individually stored blocks. The host’s software will likely split the data storage area into DataChunk areas of between 20 and 200 GBytes in size. It is recommended to leave a certain amount of storage at the end of the NVMe reserved for additional free blocks to assist with the NVMe’s wear bad blocks system and probably reduce write latency. The data chunks will align to a 4 kByte boundary. It might be good to align them to an NVMe erase block boundary (possibly 1 MByte depending on NVMe), we will determine this later in the project.
The NVMe storage registers indicate the starting block and how many blocks to write.
# NvmeStorage core interfaces
The NvmeStorage core has the following interfaces:
## Hardware interface
The system will use two NVMe devices operating in parallel to achieve the data rate required. It may be possible in the future to use a single NVMe device operating over a Gen4 PCIe interface if Ultrascale+ FPGA’s are used and a very high performance Nvme is available. The overall design can handle that eventuality, but it would need changing to support 256 bit data widths..
The NVMe PCIe devices will require a low jitter PCIe clock for operation. The design is based on there being a single external 100 MHz PCIe clock chip driving both NVMe devices and the FPGA’s differential reference clock inputs next to the GTH/GTY transceivers that will be used for NVMe PCIe communications. The GTH/GTY transceivers used will have to be located near the PCIe hard blocks used for NVMe communications in the FPGA so they can be used by the PCIe core. See the Xilinx information on the particular FPGA that will be used. For the xcku040-ffva1156-2-e, as used on the XKU105 development board, the pins to be used are fixed and described in the “Test FPGA resources” section of the DuneNvmeStorageDesign document.
Note that we need to be able to drive the nvme_reset_n line in order to be able to reset the Nvme devices.
The pin interfaces will thus be:
Item	Bits	Notes
nvme_clk_p	1	100 MHz PCIe clock plus input
nvme_clk_n	1	100 MHz PCIe clock neg input
nvme_reset_n	1	Output driving external NVMe’s reset

nvme0_exp_txp	4	PCIe TX lanes plus
nvme0_exp_txn	4	PCIe TX lanes neg
nvme0_exp_rxp	4	PCIe RX lanes plus
nvme0_exp_rxn	4	PCIe RX lanes neg

nvme1_exp_txp	4	PCIe TX lanes plus
nvme1_exp_txn	4	PCIe TX lanes neg
nvme1_exp_rxp	4	PCIe RX lanes plus
nvme1_exp_rxn	4	PCIe RX lanes neg

The PCIe lanes will be operating at 8 GT/s speeds, so track impedance and routing will be critical.
## Clocks and reset
The NvmeStorage block accepts a single 250 MHz clock that all of its control and data interfaces is synchronised to. Within the block its operation is synchronised to a separate 250 MHz clock derived from the NVMe PCIe external clock input. The NvmeStorage core handles the clock domain crossings.
There is a single, active high, reset signal that is used to reset the core and the external NVMe devices.
Item	Bits	Notes
clk	1	250 MHz clock input for data interfaces
reset	1	Active high reset input

## Axi4-Lite bus interface
The Axi4-lite bus interface provides host access to a set of control and status registers. It has the following ports all synchronise to the main data clock:
Item	Bits	Notes
axilOut.awready	1	Write address ready input
axilIn.awvalid	1	Write address valid input
axilIn.awaddr	4 bits	Write address, address input

axilOut.wready	1	Write data ready output
axilIn.wvalid	1	Write data valid input
axilIn.wdata	32 bits	Write data, data input
axilIn.wstrb	N/A	Not used

axilIn.bready	1	Write response ready input
axilOut.bvalid	1	Write response valid output
axilOut.bresp	2	Write response, “00” is Ok output.

axilOut.arready	1	Read address ready output
axilIn.arvalid	1	Read address valid input
axilIn.araddr	4 bits	Read address, address input

axilIn.rready	1	Read data ready input
axilOut.rvalid	1	Read data valid output
axilOut.rdata	32 bits	Read data, data output
axilOut.rresp	2	Read response, “00” is Ok output.

## NVMe write data stream
This accepts the Dune data on an AXI4-Stream interface at up to 4 GBytes/s. Its specification is:
Item	Info	Notes
Clock	250 MHz
Bus width	256 bits	4 GBytes per second interface (actually peak of 250e6 * 32 Bytes/s)
Data length	Multiple of 4 kBytes	The NVMe will expect a stream of data which is a multiple of 4 kBytes, the tlast signal being set on the last data transfer in a 4 kByte block.

The core has a degree of data buffering of the data streams, but this will not be sufficient to handle all NVMe latencies. The dataInReady line will be low when the buffers are full. It is expected that the FPGA’s large SDRAM buffer will have sufficient space to buffer the data for about 1 second to handle this latency.
If this external buffer is getting too full, some means of dropping data needs to be provided to handle extreme Nvme latencies. We are unsure as yet what the peak latencies of the Nvme drives will be.
The core provides the user with two methods of achieving flow control: an externally controlled method and an internal to the NvmeStorage core method.
If handled by the external logic, this can drop 4 kByte blocks based on the state of its buffer.
If handled, by the NvmeStorage module, then the external logic would set the dropPackets input high when the external logic’s buffer is getting too full. When this occurs the NvmeStorage core will drop complete 4 kByte blocks from the data input FIFO and increment its packets dropped register. This register can then be directly read by the host’s software at the end of a capture cycle.
We don’t expect this dropping of packets to be used unless there are significant NVMe latencies for some reason. The NVMe data will have missing packets in this case. It is assumed that the data reading software can detect this from the packet headers/trailers in the 4 kByte blocks.
Item	Bits	Notes
dataEnable	1	Enable data input for a chunk of data
dataEnabledOut	1	This is set high when the NvmeStorage unit is enabled to save data. Useful to start and reset test signal generators etc.
dropPackets	1	Set to 1 if the external logics buffer is getting too full. The NvmeStorage block will drop complete input packets and store the number of dropped packets in its registers while this is high. / If external logic is handing the dropping of packets this can be tied to 0.
AXI4-Stream
dataIn_ready	1	Ready for data output.
dataIn.valid	1	Data is valid input
dataIn.last	1	Last word of data packet input. This is used to indicate the end of a 4 kByte block.
dataIn.data	256 bits	The data input

## NVMe ToHost Control/Data stream
This AXI4 stream is used to send the Nvme stored data blocks to the host computer when reading the data. It is also used to return Nvme responses to requests issued on the FromHost control stream if this is used. It is a AXI4-Stream interface at up to 4 GBytes/s. Its specification is:
Item	Info	Notes
Clock	250 MHz
Bus width	128 bits	4 GBytes per second interface (actually 250e6 * 16 Bytes/s)
Data length	128 Byte packets	The raw PCIe write data stream will be sent with the Xilinx PCIe blocks data headers

Item	Bits	Notes
hostRecvReady	In 1	Ready for data, input.
hostRecv.valid	Out 1	Data is valid output
hostRecv.last	Out 1	Last word of packet. Set at the end of each data packet.
hostRecv.data	Out 128 bits	The data output (bits 0-31 Dword0, bits 32-63 Dword 1)
hostRecv.keep	Out 4 bits	One bit for each 32bit word that is present in the 128 bits being transferred.

The stream passes a form of PCIe TLP packets from the NVMe devices to the host. These are likely to contain 128 or 256 bytes of data depending on the PCIe max payload size in use. The packet structure is based on the Xilinx Pcie Gen3 hard blocks “TLP” packets the following describing the main fields used:
DWord (32bits)	Value	Description
0	0xNSAAAAAA	The destination address with destination identifiers. This will have the NVME identified in the topmost 4 bits, the stream in bits 24-27 and the byte address of the data. Note that for read data blocks this address will wrap around as the upper address bits, above bit 23, will not be provided.
1	0	Not used
2	0x0000XXXX	This has the number of DWords in the packet data in the bottom 11 bits and bit 12 set to 1 to indicate a write request
3	0xXXXXXXXX	Not used
4 -n	...	The following DWords contain the data

When replies to requests sent on the FromHost stream are sent on this stream the replies, if there are any, will be the raw PCIe reply packets from the NVMe devices. These are likely to contain 128 or 256 bytes of data depending on the PCIe max payload size in use. These will have the following data structure:
DWord (32 bits)	Value	Description
0	0x0BBBEAAA	B: Byte count, E: Error, A: Address
1	0x000SUCCC	S: Stream, U: Status, C: DWord count
2	0x800000TT	Reply bit set and T: request tag

Bit 95 of the header (DWord 2 bit 31) is set to 1 for replies and 0 for requests so the type of packet can be determined.
See the section on the Read Blocks system and the Communication with the Nvme for more information.
## NVMe FromHost Control/Data stream
This is an optional stream to send PCIe request packets to the Nvme devices. Requests should match the Xilinx Pcie Gen3 hard blocks “TLP” request packets. Responses will be sent on the ToHost Control/Data stream with appropriate headers. This interface can be used to enquire NVMe status information and configure the NVMe devices. It is a AXI4-Stream interface at up to 4 GBytes/s. Its specification is:
Item	Info	Notes
Clock	250 MHz
Bus width	128 bits	4 GBytes per second interface (actually 250e6 * 16 Bytes/s)
Data length	128 Byte packets	The raw PCIe write data stream needs to be sent with the Xilinx PCIe blocks data headers

Item	Bits	Notes
hostSendReady	Out 1	Ready for data, output.
hostSend.valid	In 1	Data is valid input. Set to 0 if the control interface is not used.
hostSend.last	In 1	Set to 1 in the last word of the packet.
hostSend.data	In 128 bits	The data input (bits 0-31 Dword0, bits 32-63 Dword 1)
hostSend.keep	In 4 bits	One bit for each 32bit word that is present in the 128 bits being transferred.

Please see the section “Communication with the Nvme” for more details on how to use the fromHost and toHost interfaces to communicate with the Nvme devices.
# Control and status registers
The NvmeStorage core is controlled using a set of registers likely accessed from a host computer over the modules AXI4-Lite bus interface. It is designed for host computer configuration and control of the NVMe storage system. The interface implements the following registers.
Item	Address	Bits	Notes
ID register	0x0000	32 bits	The NvmeStorage storage core type (0x56, Top 8 bits) and the version number (8.8.8 bits)
Control	0x0004	32 bits	The control register
Status	0x0008	32 bits	The status register
TotalBlocks	0x000C	32 bits	The total number of blocks available
BlocksLost	0x0010	32 bits	The number of blocks lost

DataChunkStart	0x0040	32 bits	The data chunk’s starting block number
DataChunkSize	0x0044	32 bits	The data chunk size in 4/8k blocks
Error	0x0048	32 bits	Information on the errors
NumBlocks	0x004C	32 bits	The number of blocks written
TimeUs	0x0050	32 bits	The time in microseconds since the start of the capture
PeakLatency			We might implement this

ReadControl	0x0080	32 bits	Read data control
ReadStatus	0x0084	32 bits	Read data status
ReadBlock	0x0088	32 bits	The starting 4 kByte read block number
ReadNumBlocks	0x008C	32 bits	The number of blocks to read

Nvme0 Registers. Same as main set above
ID register	0x0100	32 bits	The NvmeStorage storage core type (0x56, Top 8 bits) and the version number (8.8.8 bits)
...

Nvme1 Registers. Same as main set above
ID register	0x0200	32 bits	The NvmeStorage storage core type (0x56, Top 8 bits) and the version number (8.8.8 bits)
...

The Nvme0 and Nvme1 sets of registers directly access the individual Nvme engines of the two Nvme devices. The standard set of registers, starting at address 0, provide access to both Nvme0 and Nvme1 simultaneously when written too. The read values of these will be from Nvme0 only. (Maybe error is generated from both sources ?)

## Control Register
The control register controls the overall system.
Item	Bits	Notes
Reset	0	Set high to reset/initialise the system
Initialise	1	Software set to 1 to start initialisation (Normally initialised by Reset)
DataEnable	2	Enable data import when set high. When reset to 0 data import will be stopped.
ClearError	3	Set high to clear the Error status bit
ClearBlocksLost	4	Set high to clear the BlocksLost status bit and BlocksLost register

The Reset bit, when set high, will instigate a reset of the module and the Nvme devices.
If the core is configured to initialise on reset, then it will itself initialise the Nvme devices. The Initialise bit will be set high when it has completed this process. Do not communicate with the Nvme’s before this bit is set high. If the core is not configured to initialise the Nvme’s on reset, then the software can either manually configure the Nvme’s or set the Initialise bit high to instigate this process.
## Status Register
Item	Bits	Notes
Reset	0	When high reset is in progress
Initialised	1	When high the system has completed initialisation
DataEnabled	2	Data import is enabled
Error	3	An error has occurred
BlocksLost	4	Some data blocks have not been written correctly due to timeouts or other reasons. Only available if the internal data block dropping system is used.

## Read Blocks System
The read block system will send the block data over a AXI4-Stream interface that can be connected to a Xilinx PCIe DMA core and be read using the Linux XDMA or other such driver driver.

In order to read data blocks the host computer should set the ReadBlock register to the starting block number and the ReadNumBlocks to how many blocks to read. When the ReadControl register’s ReadEnable bit is set the NvmeStorage core will read the data from the Nvme devices and send the resulting data as Pcie “TLP” packets to the host over toe ToHost AXI4 stream.
The bottom 23 bits of the address field in the Pcie packets header can be used to determine the packets are block read data and are in the correct sequence. (We could change the system to use 64bit addressing if needed).
### Read Control Register
Item	Bits	Notes
ReadEnable	0	Set high to start reading data from the given block number. Set low to stop reading. Will also be set low by the hardware when the number of programmed blocks has been read

### Read Status Register
Item	Bits	Notes
ReadEnabled	0	When high indicates the reading of data is in progress.

# Communication with the Nvme
This section will describe how to communicate directly with the Nvme devices over the FromHost/ToHost Pcie packet streams. For now the DuneNvmeStorageDesign document can be consulted along with the Xilinx PCie Gen 3 hard block document PG156 and the Nvme Express Revsion 1.3 specification document.
In essence the host computer can send Nvme register read/write requests and also send an Nvme admin or read/write data IO request over the FromHost AXI4 stream. The NvmeStorage’s request/reply queue engine can be used to simplify sending and receiving queued requests and replies. Responses to these request packets are sent to the host over the ToHost AXI4 Stream.
TBD
# Testing the NvmeStorage core
See the NvmeStorageDesign manual for details.
## NVMe Devices
The NVMe devices used during the development and testing were (all 512 GByte versions):
Manufacturer	Device	Version	Endurance	Notes
Samsung	970 Pro	Gen3,1.3	600 TB	2.3 GBytes/s, 5.2W, Samsung Phoenix controller
WD	Black SN750	Gen3,1.3	300 TB	2.6 GBytes/s, WD NVMe Architecture Controller / MaxPayloadSize: 512 Bytes / PcieCapabilities: 0xC0
Seagate	FireCuda 520	Gen4,1.3	850 TB	2.5 GBytes/s, Phison E16 Controller / MaxPayloadSize: 256 Bytes / PcieCapabilities: 0x80

Others
Samsung	970 EVO Plus	Gen3,1.3	300 TB	3.2 GByes/s, 9W, Samsung Phoenix controller
Seagate	BarraCuda 510	Gen3,1.3	320 TB	2.1 GBytes/s, 4.6W, Phison E12 Controller
Corsair	Force MP510	Gen3,1.3	800 TB	2 GBytes/s, 4.8W, Phison E12 Controller

List of some other devices: https://en.wikipedia.org/wiki/List_of_Intel_SSDs
# Notes
When running at full data rate these device could use around 25 Watt’s of heat, so cooling systems will need to be implemented.