Dune NVMe Storage Manual
Preliminary

Project	DuneNvme
Date	2020-04-08
Reference	DuneNvmeStorageManual-2
Author	Dr Terry Barnaby

# Introduction
This document covers the use of the Dune NVMe Storage Fpga core and testing thereof. There is also a design level manual, DuneNvmeStorageDesign which covers detailed implementation information and notes.
# Overview
The Dune Neutrino experiment has two neutrino detection chambers. Each chamber has a matrix of wires and electronics to amplify and digitise signals captured from neutrino interactions in the chambers. The digitised data is passed through optical fibres to 300 FPGA data processing engines installed in conventional x86 computer servers. The fibres to each FPGA carry around 60 GBits/s of data plus extra bits for encoding overheads.
The Dune project will be designing a custom FPGA board to be installed into the multiple host server computers. This FPGA board will convert the optical data streams to electrical signals, compress and process this data. Currently a simple compression algorithm is proposed that provides around a 2:1 compression ratio. The resulting 3.5 GBytes/s, approx, data stream will be stored in a DDR4 RAM based buffer that can store up to 10 seconds worth of data.
The overall requirement of the NvmeStorage core is to store, real-time, the raw data stream from the Dune system and be able to, with a slower access rate, read that data. The full system is able to store 120 TeraBytes of incoming data at a rate of 600 GigaBytes per second across its multiple FPGA based data processing engines.
For each FPGA engine the source data consists of fixed sized chunks (bursts) of data that are from 20 to 200 GBytes in size. These data chunks are stored, round robin fashion, into the NVMe devices with a new chunk overwriting the oldest chunk written.
The host server computer controls the overall operation of the system via a PCIe interface. It is able to lock a particular chunk in NVMe storage against subsequent writes if it contains data of interest. The data from this chunk can then be read out by the host computer.
## Dune Raw Data
For information, the raw data from the Dune sensors consist of 2560 wires sampled with 12 bits resolution. A packet containing 64 sets of this data will likely be generated, that includes a start time field and other control information. This will yield data packets of a size near 128 kBytes after compression.
The NvmeStorage core will store data with a block size granularity of 8 kBytes (2 x 4096 NVMe blocks). If an NVMe error occurs the system will continue storing data, if it can, keeping the block numbers consistent. This means that there could be a set of blocks with in-valid data. So some method of determining if a packet of data is corrupt is needed. The compression algorithm used will provide variable length blocks. We suggest using a variable length packet with CRC checksum padded to a 8 kByte boundary. So a data packet for 64 * 2560 x 12 bit wire samples could look line:
Item	Length	Notes
Length	32 bits	The compressed data length in bytes (packet length is this field + timestamp + misc header length + CRC length).
Timestamp	64 bits	Timestamp for data
Misc	?	Extra header information as needed
Compressed samples	~122 kBytes	The compressed data for 64 samples of 2560 wires at 12 bit resolution.
CRC	32 bits	CRC32 checksum
Padding	?	Padding to next 4 kByte boundary

The actual packet format is irrelevant to the NVMe storage system. It simply stores data in blocks to a 8 kByte boundary. However, due to possible latency issues the NVMe may have to drop data and this needs to be handled in a way that allows the host software to use the resulting data stream and understand when data has been lost. To do this the data stream needs to be blocked into some sized packet with a suitable header and dropped at that chunk size.
Two possible methods are:
1. Store and drop at the super packet (128 kByte) level.
2. Introduce a smaller storage packet size of say 8 or 16 kBytes. This packet would have some header to allow the software to understand if some of these 8/16 k packets are missing. This could be two 16bit values: the super packet number and the 8/16k packet number within the super packet.
When a packet is sent across the AXI4-Stream, the tlast signal will need to be set in the last 128bit data item of whatever packet size is chosen. Also, if a whole super packet is to be stored as a chunk, the max size of this compressed packet has to be known to the NvmeStorage block.
Using a fixed sized 8/16 kByte storage packet would likely be easiest to handle and be most efficient, but there is the chance or a larger number of full super packets being corrupted.
# NvmeStorage core operation
On a hardware line driven or register driven reset the NvmeStorage system will enter an initialisation state. During this state either the core or perhaps the host will setup the NVMe devices for operation (yet to be decided which). Once initialised the core is ready to accept data and/or commands to read data.
A new data chunk is start by setting the dataEnable register bit or the hardware dataEnable line. Data will be written to the NVMe devices until either the dataEnable register bit is reset or the dataEnable line goes low. At this point the dataChunk number will be incremented ready for the next data chunk to be imported.
The NvmeCore will respond to data read requests as commanded by the host cpu writing to the read control registers.
## NVMe Storage Access
The NvmeStorage will use a block size of 4 kBytes. The NVMe storage will use a simple integer block number to address the individually stored blocks. The NVMe storage will be split into data chunk areas of between 20 and 200 GBytes in size. There will be, a register settable, fixed size for these and up to 16 data chunks will be supported.
A certain amount of storage at the end of the NVMe will be reserved for additional free blocks to assist with the NVMe’s wear bad blocks system. The data chunks will align to a 4 kByte boundary. It might be good to align them to an NVMe erase block boundary (possibly 1 MByte depending on NVMe), we will determine this later in the project.
The NVMe storage registers indicate which chunk number is currently being written to and have a set of lock bits to lock (prevent overwrite) a data chunk. If a data chunk is locked the system will move over this chunk and start writing to the next available chunk.
# NvmeStorage core interfaces
The NvmeStorage core has the following interfaces:
## Hardware interface
The system will use two NVMe devices operating in parallel to achieve the data rate required. It may be possible in the future to use a single NVMe device operating over a Gen4 PCIe interface if Ultrascale+ FPGA’s are used. The overall design can handle that eventuality.
The NVMe PCIe devices will require a low jitter PCIe clock for operation. We will base our design on there being a single external 100 MHz PCIe clock chip driving both NVMe devices and the FPGA’s differential reference clock inputs next to the GTH/GTY transceivers that will be used for NVMe PCIe communications. The GTH/GTY transceivers used will have to be located near the PCIe hard blocks used for NVMe communications in the FPGA so they can be used by the PCIe core. See the Xilinx information on the particular FPGA that will be used. For the xcku040-ffva1156-2-e, as used on the XKU105 development board, the pins to be used are fixed and described in the “Test FPGA resources” section of the DuneNvmeStorageDesign document. The pin interfaces will thus be:
Item	Bits	Notes
nvme_clk_p	1	100 MHz PCIe clock plus input
nvme_clk_n	1	100 MHz PCIe clock neg input
nvme_reset_n	1	Output driving external NVMe’s reset

nvme0_exp_txp	4	PCIe TX lanes plus
nvme0_exp_txn	4	PCIe TX lanes neg
nvme0_exp_rxp	4	PCIe RX lanes plus
nvme0_exp_rxn	4	PCIe RX lanes neg

nvme1_exp_txp	4	PCIe TX lanes plus
nvme1_exp_txn	4	PCIe TX lanes neg
nvme1_exp_rxp	4	PCIe RX lanes plus
nvme1_exp_rxn	4	PCIe RX lanes neg

The PCIe lanes will be operating at 8 GT/s speeds, so track impedance and routing will be critical.
## Clocks and reset
The NvmeStorage block accepts a single 250 MHz clock that all of its control and data interfaces is synchronised to. Within the block its operation is synchronised to a separate 250 MHz clock derived from the NVMe PCIe external clock input. The NvmeStorage core handles the clock domain crossings.
There is a single, active high, reset signal that is used to reset the core and the external NVMe devices.
Item	Bits	Notes
clk	1	250 MHz clock input for data interfaces
reset	1	Active high reset input

## Axi4-Lite bus interface
The Axi4-lite bus interface provides host access to a set of control and status registers. It has the following ports all synchronise to the main data clock:
Item	Bits	Notes
axilOut.awready	1	Write address ready input
axilIn.awvalid	1	Write address valid input
axilIn.awaddr	4 bits	Write address, address input

axilOut.wready	1	Write data ready output
axilIn.wvalid	1	Write data valid input
axilIn.wdata	32 bits	Write data, data input
axilIn.wstrb	N/A	Not used

axilIn.bready	1	Write response ready input
axilOut.bvalid	1	Write response valid output
axilOut.bresp	2	Write response, “00” is Ok output.

axilOut.arready	1	Read address ready output
axilIn.arvalid	1	Read address valid input
axilIn.araddr	4 bits	Read address, address input

axilIn.rready	1	Read data ready input
axilOut.rvalid	1	Read data valid output
axilOut.rdata	32 bits	Read data, data output
axilOut.rresp	2	Read response, “00” is Ok output.

## NVMe write data stream
This accepts the Dune data on an AXI4-Stream interface at up to 4 GBytes/s. Its specification is:
Item	Info	Notes
Clock	250 MHz
Bus width	128 bits	4 GBytes per second interface
Data length	Multiple of 4k	The NVMe will expect a stream of data which is a multiple of 4 kBytes

The core has a degree of data buffering of the data streams, but this will not be sufficient to handle all NVMe latencies. The dataIn.ready line will be low when the buffer is full. It is expected that the FPGA’s DMA buffer will have sufficient space to buffer the data for about 1 second to handle this latency.
If the outside logics input buffer is getting too full it should set the dropPackets input. When this occurs the NvmeStorage core will drop a complete input packets from the tail of its input FIFO and increment its packets dropped counter. We don’t expect this to be used unless there are significant NVMe latencies for some reason. The NVMe data will thus have missing packets in this case. It is assumed that the data reading software can detect this from the packet headers.
Item	Bits	Notes
dataEnable	1	Enable data input for a chunk of data
dropPackets	1	Set to 1 if the input buffer is getting too full. The NvmeStorage block will drop complete input packets and store the number of dropped packets in its registers while this is high.
AXI4-Stream
dataIn.ready	1	Ready for data output. Holds data input for some maximum time
dataIn.valid	1	Data is valid input
dataIn.last	1	Last word of data packet input. This is used to indicate the end of a contiguous packet of data. This could be an 8/16 k packet or a ~128k super packet (TBD).
dataIn.data	128 bits	The data input

## NVMe read data stream
This send the data block packets to the host computer when reading the data. It is a AXI4-Stream interface at up to 4 GBytes/s. Its specification is:
Item	Info	Notes
Clock	250 MHz
Bus width	128 bits	4 GBytes per second interface
Data length	128 Byte packets	The raw PCIe write data stream will be sent with the Xilinx PCIe blocks data headers

Item	Bits	Notes
dataOut.ready	1	Ready for data input.
dataOut.valid	1	Data is valid output
dataOut.last	1	Last word of data chunk output. Set at the end of each data packet.
dataOut.data	128 bits	The data output (bits 0-31 Dword0, bits 32-63 Dword 1)

The read data packets will be the raw PCIe write data packets from the NVMe devices. These are likely to contain 128 or 256 bytes of data depending on the PCIe max payload size in use. These will have the following data structure (Not yet decided):
DWord	Value	Description
0	0xNSAAAAAA	The destination address with destination identifiers. This will have the NVME identified in the topmost 4 bits, the stream in bits 24-27 and the byte address of the data based on 0 being the beginning of the read request in the remaining bits. Note this address will wrap around in that the upper address bits above bit 23 will not be provided.
1	0	Not used
2	0x0000XXXX	This has the number of DWords in the packet data in the bottom 11 bits and bit 12 set to 1 to indicate a write request
3	0xXXXXXXXX	No used
4 -n	...	The following DWords contain the data

## NVMe control data stream
This is an optional stream to send PCIe packets to the Nvme devices. Responses will be sent on the read data stream with appropriate headers. This interface can be used to enquire NVMe status information and configure the NVMe devices. It is a AXI4-Stream interface at up to 4 GBytes/s. Its specification is:
Item	Info	Notes
Clock	250 MHz
Bus width	128 bits	4 GBytes per second interface
Data length	128 Byte packets	The raw PCIe write data stream needs to be sent with the Xilinx PCIe blocks data headers

Item	Bits	Notes
controlIn.ready	1	Ready for data output.
controlIn.valid	1	Data is valid input
controlIn.last	1	Last word of data chunk input. Set at the end of each data packet.
controlIn.data	128 bits	The data input (bits 0-31 Dword0, bits 32-63 Dword 1)

The read data packets will be the raw PCIe write data packets from the NVMe devices. These are likely to contain 128 or 256 bytes of data depending on the PCIe max payload size in use. These will have the following data structure (Not yet decided):
DWord	Value	Description
0	0xNSAAAAAA	The destination address with destination identifiers. This will need the NVME identified in the topmost 4 bits, the stream in bits 24-27 and the byte address of the data based on 0 being the beginning of the read request in the remaining bits. Note this address will wrap around in that the upper address bits above bit 23 will not be provided.
1	0	Not used
2	0x0000XXXX	This has the number of DWords in the packet data in the bottom 11 bits and bit 12 set to 1 to indicate a write request
3	0xXXXXXXXX	Not used
4 -n	...	The following DWords contain the data

# Control and status registers
The NVMe control interface is implemented using an AXI4-Lite bus interface. It is designed for host computer setup and control of the NVMe storage system. The interface implements the following registers.
Item	Address	Bits	Notes
ID register	0x0000	32 bits	The NVMe storage core type (Top 8 bits) and the version number (8.8.8 bits)
Control	0x0004	32 bits	The control register
Status	0x0008	32 bits	The status register
Errors	0x000C	32 bits	Information on the errors
BlocksLost	0x0010	32 bits	The number of blocks lost (Might use Packets lost)
Data Chunk Size	0x0014	32 bits	The data chunk size in 4k blocks
ReadControl	0x0018	32 bits	Read data control
ReadBlock	0x001C	32 bits	The starting 4 kByte read block number
ReadNumBlocks	0x0020	32 bits	The number of blocks to read

The read block system will send the block data over a AXI4-Stream interface that can be connected to a Xilinx PCIe DMA core and be read using the Linux XDMA driver.

## Control Register
Item	Bits	Notes
Reset	0	Set high to reset/initialise the system
Initialised	1	Software drive initialisation completed
DataEnable	2	Enable data import. When reset to 0 data import will be stopped and the DataChunkNum register will be incremented.
ClearError	3	Set high to clear the Error status bit
ClearBlocksLost	4	Set high to clear the BlocksLost status bit
ClearChunkOverrun	5	Set high to clear the ChunkOverrun status bit

DataChunkLocks	12:27	Each bits locks a data chunk area for write storage. Up to 16 data chunk areas are supported

## Status Register
Item	Bits	Notes
	0	Not used
Initialised	1	When high the system has completed initialisation
DataEnabled	2	Data import is enabled
Error	3	An error has occurred
BlocksLost	4	Some data blocks have not been written correctly due to timeouts or other reasons
ChunkOverrun	5	Data import would have cross a boundary. Import data from then on is being ignored.

DataChunkNum	8:11	The current data chunk area being written to
DataChunkLocks	12:27	Indicates the data chunk areas that are locked for write

## Read Control Register
Item	Bits	Notes
ReadEnable	0	Set high to start reading data from the given block number. Set low to stop reading. Will also be set low by the hardware when the number of programmed blocks has been read

# Testing the NvmeStorage core
TBD
## NVMe Devices
The NVMe devices used during the development and testing were (all 512 GByte versions):
Manufacturer	Device	Version	Endurance	Notes
Samsung	970 Pro	Gen3,1.3	600 TB	2.3 GBytes/s, 5.2W, Samsung Phoenix controller
WD	Black SN750	Gen3,1.3	300 TB	2.6 GBytes/s, WD NVMe Architecture Controller
Seagate	FireCuda 520	Gen4,1.3	850 TB	2.5 GBytes/s, Phison E16 Controller

Others
Samsung	970 EVO Plus	Gen3,1.3	300 TB	3.2 GByes/s, 9W, Samsung Phoenix controller
Seagate	BarraCuda 510	Gen3,1.3	320 TB	2.1 GBytes/s, 4.6W, Phison E12 Controller
Corsair	Force MP510	Gen3,1.3	800 TB	2 GBytes/s, 4.8W, Phison E12 Controller

List of some other devices: https://en.wikipedia.org/wiki/List_of_Intel_SSDs
# Notes
When running at full data rate these device could use around 25 Watt’s of heat, so cooling systems will need to be implemented.